LASSI_DAQ Scanner Control
### 1.0 Introduction
The LASSI data acquisition and control program (lassi_daq) is a Windows application, written in C#. The program is responsible for:
1. Providing a control and data network interface to both the LASSI manager and post-processing programs;
2. Control of the deployment/retraction of the Terrestrial Laser Scanner (TLS) from its weather protective enclosure (TBD);
3. Control of the TLS, including the remote power off/on switch powering the unit;
4. Configuration and sequencing and initiation of a TLS scan;
5. Retrieval of the TLS data, and formatting the data for publishing to both the LASSI manager and post-processing programs;
6. Reporting errors due to deployment, misconfiguration, or TLS error conditions to the LASSI manager.
The following sections detail the sequence of operations and interactions between the lassi_daq, the post-processing and the LASSI manager.

### 2.0 Basic Sequence of Operation

Lassi DAQ
Lassi Manager
Pipeline
Active
Surface

Run scan

Mount

Deploy [2.1

TLS Ready [2.3]

Start TLS Scan [2.5]

Scan Complete

Scanner TLS Data [2.6]

Scanner Data

TLS Configure [2.4]

TLS
Send configuration

Connect/Subscribe

Power up [2.2]

TLS Deployed

Status Updates[1]

Pipeline results

Update Z’s (non-ref scan only [3])

Start + Reference Scan Information

Connect/Subscribe

Scanner Data

Power down TLS [2.7]

Stow TLS [2.8]

TLS Stowed

### 2.1 TLS Deployment
The initial state is that the unit is in its stowed position. The interface for stow/unstow are TBD. When a scan is requested, the TLS mount will be commanded to deploy for operation. If the use case is to leave the TLS in its deployed position between measurements, then this step will just confirm the TLS is in the deployed position.
### 2.2 TLS Power up
Via a remote power switch or power strip (e.g. ‘iboot bar’), power is applied to the unit. It should be noted that once shutdown, the unit should not be re-powered on for a TBD interval, to allow residual voltages to bleed off. (TODO: Why is this important? It seems that the unit if shutdown remotely, does not power back up if power is re-applied too soon. ) The unit powers up and boots up. This operation can be performed in parallel with the deployment operation.
Issue: We may need an interval timer to prevent short power-off periods.
### 2.3 TLS Network Connection
In order for the unit to connect onto a network, it must first be assigned an IP address via DHCP. Once assigned an address, the unit listens for broadcast messages from the LASSI DAQ program. A connection is negotiated by responding to the broadcasts with an ‘I am here’ message. The lassi_daq program will monitor and try to initiate connection after power is applied to the TLS.
### 2.4 Setup
The LASSI DAQ program monitors the status of the instrument. Once the lassi_daq detects a status of ready, it will proceeds to specify the scan parameters, such as:
- range vs. speed (select range)
- distance (100m)
- scan field of view (FOV)
- number of image points
- project name
- weather temp, press, and atmospheric scale (PPM)
### 2.5 Execute Scan
The execute scan event is sent to the device. The device executes whatever calibrations are necessary and then begins the scan. [TODO: At this point it is unclear whether or not the time (1 PPS) input will be used to synchronize time, or whether the measure event output are used.] The LASSI DAQ monitors the scanner status to monitor scan progression.
### 2.6 Scan Data Transfer/Export
Once the scan is complete, calls are made to the TLS API to extract the TLS scan data, and then publishes the scan data to both the LASSI manager (which write a FITS file for archival purposes) and the post-processing programs.
[TODO: Normally the raw scan data is recorded onto an internal high speed disk. I currently do not see a mechanism to directly access this data to ‘stream’ the data.]
### 2.7 Scanner Power Down
Once the scan is complete, and the data has been transferred, the LASSI DAQ will issue a power-down event to the scanner, and the TLS performs an orderly shutdown. A timer will delay for a period and then remove power from the TLS unit.
### 2.8 TLS Retract/Stow
When requested (depending upon the use case selected) the lassi_daq will command the mount to retract/stow the unit into its weather protective enclosure.
[TODO: A question needing to be answered is what will the policy with respect to the TLS mount. Should it remain in the deployed state during the entire observing session, or retracted in between measurements. If it remains deployed, what mechanism/event stows it? Is there a risk of ‘forgetting’ its deployed?]

### 3.0 LASSI Interfaces
The primary interface used by both the LASSI manager and the post-processing programs is implemented using 0MQ (pronouced ‘zero-M-Q’) communications library, and the Mesgpack data encodings. The communications pattern will be via PUSH/PULL pair for commands and status requests, and PUB-SUB for asynchronous results and data.
### 3.1 Deploy/Retract TLS
Interface is TBD.
### 3.2 TLS Power Control
As an example, the ‘iboot’ remote control power strip is commanded using an HTTP protocol. The actual unit to be used for this is TBD.
### 3.3 Specify and Perform Scan
The scan parameters will be specified by the LASSI manager. The scan parameters and start message can be sent without waiting for the TLS deployment/power-up. The lassi_daq will handle the sequencing of the required steps.
Scan Parameters:
- Field of view (center instrument az, el and delta az, delta el)
- sensitivity
- resolution (usually specified as x mm @ 10m)
- EDM mode (speed vs. range) [TODO: define EDM]
- Remove low intensity pixels
- Remove filtered/overloaded pixels
### 3.4 Return/Export Data
The LASSI DAQ program will emit status periodically over the PUB-SUB connection to indicate the state of the scan. At scan completion, TLS data will be published to the PUB connection endpoint.
### 3.5 Scan Metadata
The following scan metadata will be returned when requesting image data:
- orientation matrix – TBD currently unused in processing
- ambient conditions (temp, press) as reported by TLS
- TLS project, scan number (Not to be confused with GBT project and scan number)
### 4.0 Software Specifics
### 4.1 Design Constraints
### 4.1.1 Windows/C# Programming Environment
The lassi_daq will require a windows machine to be run on. The driver for this decision is a constraint that the TLS vendor (Leica) imposes by their application programming interface (API) libraries. The API provided supports only the C# language, running on Windows.
### 4.1.2 TLS to Host Network Configuration
The TLS and the TLS API use a ‘zero-configuration’ mechanism, where the TLS broadcasts ‘hello’ packets, and waits for the host computer to respond. This works well if the computer is directly connected to the TLS, but is incompatible with GBO site LAN systems. Thus the TLS will need to be directly connected to a host, and the host must provide DHCP services to assign an IP address to the TLS when it boots.
### 4.1.3 Threading Model
The official documentation does not specify limits on the threading environment for the API. I will note that some calls seem to be asynchronous. For example calling StartScan() returns immediately, even though the scan has yet to execute. Status queries can also be made at any time.
Looking at the ScannerAPIDemo code, I gather that many API calls are from non-UI threads/Tasks. This may require a query to Leica about thread safety of the API.
I envision a thread will be dedicated to handling the commands received via ZMQ. The same thread could also periodically gather the scanner status.
Where inter-thread communications is required, there is a ConcurrentQueue class which functions similarly to the tsemfifo template in Ygor.
### 4.2 TLS State Machine
The ScanDeviceInterface::get_state() method can be used to query the instruments state. The possible states are:
1. Ready – The scanner is powered up and ready for a command
2. Paused – The scan was running, but has been paused
3. Calculating – Not sure. Computing a result?
4. Imaging – Acquiring images (i.e. pictures, not ranges)
5. Calibrating Tilt Sensor – I expect this means what it sounds like. As a note, the tilt sensor cannot be used in the inverted mounting position.
6. Preparing Scan – Scan command has been given, but scanner is performing internal preparations to scan, like positioning mount or spinning up the mirror.
7. Scanning – Scanner is acquiring range data
8. Initializing – TBD
9. Running – TBD
10. Failure – Scanner has failed to complete an operation
The typical state sequence (from observation) is:
- Ready ⇒ Start Scan ⇒ Preparing Scan
- Preparing Scan ⇒ Scanner Ready ⇒ Scanning
- Scanning ⇒ Scan Complete ⇒ Ready

### Lassi_daq Command Protocol Details
The TLS controller will listen for command at the local port 55666. A URL would look like 'tcp://lassi.ad.nrao.edu:55666'. The command/response link are ZMQ_REQ (request) at the client end and a ZMQ_RPY (reply) at the lassi_daq (TLS scanner controller) end.
Commands and data follow the ZMQ convention of a message header followed by 0 or more data frames. ZMQ handles the details of grouping message boundaries. The headers are always a Mesgpack encoded string, which in some cases is enough to convey the message intent (e.g a start message header is simply ‘StartScan’, with no following data). Commands are always acknowledged with a Mesgpack encoded OK_ERROR data structure which conveys several items such as error code, error message string, and device status.
The lassi_daq also has a ZMQ_PUB (publish) interface which the scanner status and data are published on. A client must use a ZMQ_SUB socket to subscribe to the published data. The URL would be 'tcp://lassi.ad.nrao.edu:55668'. In addition to data, state/status changes are also published asynchronously (meaning without a query command) on the publish interface.

### Command Protocol
The following commands are used to initiate/configure the TLS controller. Where items are quoted, the data is UTF-8 encoded strings. Where the word ‘struct’ occurs, the data is encoded using msgPack. The ASCII drawn boxes shown in each command section denote a ZMQ frame boundary. Data types are described in the following section.
### Start Scan
  +-----------------+
  | "StartScan" |
  +-----------------+

* The reply will be a frame of:
  +-----------------+
  | struct OK_ERROR |
  +-----------------+
  | struct ScanInfo |
  +-----------------+

### Stop Scan
  +-----------------+
  | "StopScan" |
  +-----------------+

  * The reply will be a frame of:
  +-----------------+
  | struct OK_ERROR |
  +-----------------+

### Pause Scan
  +-----------------+
  | "PauseScan" |
  +-----------------+
  * The reply will be a frame of:
  +-----------------+
  | OK || ERROR |
  +-----------------+
  | struct OK_ERROR |
  +-----------------+

### Resume Scan
     +-----------------+
  | "ResumeScan" |
  +-----------------+

  * The reply will be a frame of:
  +-----------------+
  | struct OK_ERROR |
  +-----------------+

  Note: Only scans which have been 'paused' can be resumed. A scan which has been stopped cannot be resumed.

### Export Scan
  +-----------------+
  | "Export" |
  +-----------------+

  * The reply will be a frame of:

  +-----------------+
  | struct OK_ERROR |
  +-----------------+

  This will cause the last scan taken to be exported to the pub/sub interface.

### Configure Scan
  This updates the settings for:
- scanner project
- resolution (enum)
- quality (int)
- sensitivity (enum)
- scan mode (enum)
- Field of view (az_center, el_center, az width, el width)

  The above info is packed into a message pack encoded struct ConfScan.
  +-----------------+
  | "Configure" |
  +-----------------+
  | struct ConfScan |
  +-----------------+
* The reply will be a frame of:
  +-----------------+
  | struct OK_ERROR |
  +-----------------+

### Move to Azimuth
  +-----------------+
  | "MoveAz" |
  +-----------------+
  | struct MoveToAz |
  +-----------------+

  * The reply will be a frame of:
  +-----------------+
  | struct OK_ERROR |
  +-----------------+

### Get Status
  +-----------------+
  | GETSTATUS |
  +-----------------+

  * The reply will be a frame of:
  +-----------------+
  | struct OK_ERROR |
  +-----------------+

### Export Previous Scan From Scanner
  This should export a scan from an arbitrary project. Some scan info may not be available however.
  The ScanFrom struct contains:
- The scanner project name
- The scanner scan number

  +-----------------+
  | "ExportFrom" |
  +-----------------+
  | struct ScanFrom |
  +-----------------+
* The reply will be a frame of:
  +-----------------+
  | struct OK_ERROR |
  +-----------------+

### Delete Scan on the TLS device
  This will delete a scan stored on the device.

  +-----------------+
  | "DeleteFrom" |
  +-----------------+
  | struct ScanFrom |
  +-----------------+
* The reply will be a frame of:
  +-----------------+
  | struct OK_ERROR |
  +-----------------+
### Get Result (pyTLS local method)
  This method allows subscribed data to be accessed without a callback.

### Data Published on the ZMQ_PUB interface
  When a 'EXPORT' or 'EXPORTFROM' command is received, two elements are published. First a frame labeled 'HEADER' is sent which has all the scan configuration information. This is immediately followed by a frame labeled 'DATA'. These are intended for use by the fits writer daemon.

  +-----------------+
  | "HEADER" |
  +-----------------+
  | struct FitsHead |
  +-----------------+
  +-----------------+
  | "DATA" |
  +-----------------+
  | struct FitsData |
  +-----------------+

  On each TL scanner state change, the new state is published.
  +-----------------+
  | STATUS |
  +-----------------+
  +-----------------+
  | struct OK_ERROR |
  +-----------------+

  * This will have the scanner state info.
  * It may also contain any error messages present on the device.

  An application may also subscribe to one or more of the data columns. When a scan is exported, the union of all subscribed data columns is published. The arrays are custom encoded to support msgpack_numpy which decodes directly into a NumPy array for speed. Note: This encoding may/will suffer from incompatible endianness. If that is the case, there is a NumPy method which can byte-swap an entire array.

  The possible arrays are (listed by message headers):
- X_ARRAY – the X component of data acquired from az,el,r measurements
- Y_ARRAY – the Y component of data acquired from az,el,r measurements
- Z_ARRAY – the Z component of data acquired from az,el,r measurements
- AZ_ARRAY - instrument relative raw horizontal angles
- EL_ARRAY - instrument relative raw elevation angles
- R_ARRAY - radial distance measurements
- I_ARRAY - pixel intensity
### Subscribing to Data
  The subscribe method takes the name, or list of names of the arrays
  of interest. It also includes an optional argument of a callback, which
  should have a signature of string data, numpy_array. e.g:
  def mycallback(name, numpy_array):
      pass

  subscribe("X_ARRAY", mycallback)

  Note that the mycallback entry may be None. In that case, the subscribed data can be accessed using the get_result(name) method.

### Subscription Details
When a subscription request is processed a number of steps happen:
1. The name is validated
2. If provided, the callback is checked for the correct signature
3. If the callback subtask has not been started it is started.
4. A REQ/RPY connection is made from the call context to the callback subtask to announce the subscription. In response, the subtask calls the ZMQ setsockopt() with the subscription filter. This sets up the ZMQ subscription filter.
5. The last step is to send a subscribe_array request to the lassi_daq, to announce that the connection is interested in the subscribed data.
The reason for the dual sets of filtering is to minimize publishing traffic. One could argue that the step 4 is unnecessary, since step 5 prevents uninteresting data to be published in the first place.

### Protocol Data Structures
struct ScanInfo
{
    int scan_number;
};
Used by StartScan.

struct OK_ERROR
{
    string error_message;
    int state;
    bool is_ok;
};
Used in all command responses to acknowledge whether or not the command succeeded, any detailed error messages, and the current scanner state.

struct MoveToAz
{
    float move_to_az;
};
Used by the Move_Az command.

struct ConfScan
{
    string project;
    int scan_resolution;
    int scan_quality;
    int scan_sensitivity;
    int scan_mode;

    float center_az;
    float center_el;
    float fov_az;
    float fov_el;
};
Used by the Configure command.

struct FitsHeader;
struct FitsData;

struct ScanFrom
{
    string project;
    int scan_number;
}
Used by the ExportFrom and DeleteFrom commands.